## Slide 1: Computer Communication Networks (CMP 206)
Compiled by
Egena Onu, Ph.D.

## Slide 2: Network Layer (Layer 3)
The Network Layer, otherwise known as the Internet Layer in the TCP/IP model is the layer that holds the internet architecture together.
The job of the network layer is to permit hosts to inject packets of data into any network and have them travel independently to their destinations.
The packets may arrive at their destinations in a different order than the were sent then reassemble into the order which they were sent.
Notes: Each physical networking technology limits the amount of data that can fit in a frame
  Ethernet: 1500 octets
  FDDI: 4470 octets
This is called the network’s Maximum Transmission Unit (MTU).
Limiting datagrams to fit in the smallest possible MTU would make travelling across networks with a larger MTU inefficient
Allowing datagrams to be larger than a network’s MTU means that datagrams will not always fit in a single frame

## Slide 3: Network Layer
There are two protocols defined on the network layer to enable the forwarding and reception of data between devices on the internet:
  Internet Protocol (IP)
  Internet Control Message Protocol (ICMP)

## Slide 4: Internet Protocol (IP)
IP is the protocol used to address data packets on the internet as the move from device to device.
IP provides several features, most importantly, addressing and routing.
There are two versions of IP currently in use:
  IPv4
  IPv6

## Slide 5: IPv4
An IPv4 datagram consists of a header part and a body or payload part.
The header has a 20-byte fixed part and a variable-length optional part.
The bits are transmitted from left to right and top to bottom.
Notes: The IP header is used to support two key operations, routing and fragmentation. Routing is the mechanism that allows traffic from a given network to be forwarded to other networks, since the data link layer represents a single network for which network boundaries exist. Fragmentation refers to the breaking down of data into manageable blocks that can be transmitted over the network.

## Slide 6: IPv4
IPv4 header is as described in this in this picture showing all of its components that allows for accurate data delivery:
Notes: Next comes an unused bit, which is surprising, as available real estate in the IP header is extremely scarce. As an April Fool’s joke, Bellovin (2003) proposed using this bit to detect malicious traffic. This would greatly simplify security, as packets with the ‘‘evil’’ bit set would be known to have been sent by attackers and could just be discarded. Unfortunately, network security is not this simple.

## Slide 7: IPv4 Header Fields
Version
  This is a 4-bits field that keeps track of which version of the protocol the datagram/packet belongs to.
Differentiated Service (DS)
  DS occupies 8 bits of the packet/IP header.
  It was originally referred to as the type of service field.
  It distinguishes between different classes of service therefore allowing for various combination of reliability and speed.

## Slide 8: IPv4 Header Fields
Total Length
  This 16-bits field says the total length of everything in the packet, including the datagram (both header and data)
  The maximum length is 65,535 bytes.
Identification
  The 16-bits identification field allow the destination host to determine which packet a newly arrived fragment belongs to.
  All the fragments of a packet contains the same identification value.
Notes: Next comes an unused bit, which is surprising, as available real estate in the IP header is extremely scarce. As an April Fool’s joke, Bellovin (2003) proposed using this bit to detect malicious traffic. This would greatly simplify security, as packets with the ‘‘evil’’ bit set would be known to have been sent by attackers and could just be discarded. Unfortunately, network security is not this simple.

## Slide 9: IPv4 Header Fields
DF (Don’t Fragment)
  Is a 1-bit field related to fragmentation.
  This field is an order to the routers to not fragment the packet.
  It is originally intended to support devices incapable of putting the pieces back together again.
  It is now mostly used as part of the process to discover the path an MTU can travel along without being fragmented.
  By setting the DF field to 1, the sender knows it will either arrive in one piece, or an error message will be returned to the sender.

## Slide 10: IPv4 Header Fields
MF (More Fragments)
  MF is a 1-bit field that indicates when all fragments of a datagram have arrived.
  All fragments except the last one has this bit set to 1.
Fragment Offset
  Fragment Offset is a 13-bits field that indicates where in the current packet this fragment belongs.

## Slide 11: IPv4 Header Fields
Time to Live (TTL)
  TTL is a counter used to limit packet lifetimes.
  It counts time in seconds, allowing a maximum lifetime of 225 seconds.
  This maximum is decremented on each hop and is decremented many times when a packet is queued for a long time in a router.
  In practice, it just counts hops and the packet is discarded when the counter hits zero.
  This feature prevents packets from wandering around forever.
  When a packet is discarded, a warning message is sent to the sender.

## Slide 12: IPv4 Header Fields
Protocol
  The protocol field indicates which transport layer protocol should handle the packet.
  It is also an 8-bits field.
Header Checksum
  Checksum is useful for detecting errors while the packet travels through the network.
Source and Destination Addresses
  These are 32-bit fields used to indicate the addresses of the sender and the receiver.

## Slide 13: IPv4 Header Fields
Options
  The 32-bit option field is designed to provide an escape to allow subsequent versions of the protocol to include information not present in the original design.
  The options field is of variable length.
  Each option begins with a 1-byte code identifying the option.
  Some of the options include:
    Security: specifies how secret the datagram is.
    Strict source routing: give the complete path to be followed.
    Loose source routing: gives a list of routers not to be missed.
    Record route: makes each router append its IP address.
    Timestamp: makes each router append its address and timestamp.
Notes: The Options field was designed to provide an escape to allow subsequent versions of the protocol to include information not present in the original design, to permit experimenters to try out new ideas, and to avoid allocating header bits to information that is rarely needed. The options are of variable length. Each begins with a 1-byte code identifying the option. Some options are followed by a 1-byte option length field, and then one or more data bytes.
The Security option tells how secret the information is. In theory, a military router might use this field to specify not to route packets through certain countries the military considers to be ‘‘bad guys.’’ In practice, all routers ignore it, so its only practical function is to help spies find the good stuff more easily.
The Strict source routing option gives the complete path from source to destination as a sequence of IP addresses. The datagram is required to follow that exact route. It is most useful for system managers who need to send emergency packets when the routing tables have been corrupted, or for making timing measurements.
The Loose source routing option requires the packet to traverse the list of routers specified, in the order specified, but it is allowed to pass through other routers on the way. Normally, this option will provide only a few routers, to force a particular path. For example, to force a packet from London to Sydney to go west instead of east, this option might specify routers in New York, Los Angeles, and Honolulu. This option is most useful when political or economic considerations dictate passing through or avoiding certain countries.
The Record route option tells each router along the path to append its IP address to the Options field. This allows system managers to track down bugs in the routing algorithms (‘‘Why are packets from Houston to Dallas visiting Tokyo first?’’). When the ARPANET was first set up, no packet ever passed through more than nine routers, so 40 bytes of options was plenty. As mentioned above, now it is too small.
Finally, the Timestamp option is like the Record route option, except that in addition to recording its 32-bit IP address, each router also records a 32-bit timestamp. This option, too, is mostly useful for network measurement.

## Slide 14: Internet Control Message Protocol (ICMP)
The ICMP is an integral part of IP designed to facilitate the transmission of notification messages between gateways and source hosts where requests for diagnostic information, support of routing, and as a means of reporting errors in datagram processing are needed.
The purpose of these control messages is to provide feedback about problems in the communication environment, and does not guarantee that a datagram will be delivered, or that a control message will be returned.

## Slide 15: IPv4 Addressing
Notes: The Internet continues to grow at a phenomenal rate. This is reflected in the tremendous popularity of the World Wide Web (WWW), the opportunities that businesses see in reaching customers from virtual storefronts, and the emergence of new ways of doing business. It is clear that expanding business and public awareness will continue to increase demand for access to resources on the Internet.

## Slide 16: IP Addressing
A basic network topology
Notes: Here are a few concepts you should be familiar with:
■ An IP address is the means by which a device is identified by the IP protocol. An IP address can be assigned to a host or to a router interface. In the example in Figure 1-42, Host A is identified by IPv4 address 10.0.1.1, and Host B is identified by IPv4 address 10.0.2.2. IPv4 and IPv6 are different; we will look into the details of IPv4 and IPv6 addresses later in this section.
■ The routing table or routing database is somewhat similar to the MAC address table discussed in the previous section. The routing table contains two main pieces of information: the destination IP or network and the next-hop IP address, which is the IP address of the next device where the IP packet should be sent.
■ A default route is a special entry in the routing table that says to forward all packets, regardless of the destination to a specific next hop.
■ Packet routing refers to the action performed by the Layer 3 device to transmit a packet. When a packet reaches one interface of the device, the device will look up the routing table to see where the packet should be sent. If the information is found, the packet is sent to the next-hop device.
■ The router or IP gateway is a Layer 3 device that performs packet routing. It has two or more interfaces connected to a network segment—either a LAN segment or a WAN segment. Although a router is usually classified as Layer 3, most modern routers implement all layers of the TCP/IP model; however, their main function is to route packets at Layer 3. R1 and R2 in the example Figure are examples of routers.

## Slide 17: IPv4 Addressing
Addressing is a key function of network layer protocols.
Addressing enables data communication between hosts on the same network or on different networks.
Internet Protocol version 4 (IPv4) provides hierarchical addressing for packets that carry your data.
Note that this section is mostly focused on the IPv4 because it is currently the most widely used network addressing protocol.
Notes: A defining feature of IPv4 is its 32-bit addresses. Every host and router on the Internet has an IP address that can be used in the Source address and Destination address fields of IP packets. It is important to note that an IP address does not actually refer to a host. It really refers to a network interface, so if a host is on two networks, it must have two IP addresses. However, in practice, most hosts are on one network and thus have one IP address. In contrast, routers have multiple interfaces and thus multiple IP addresses.

## Slide 18: IPv4 Addressing
Designing, implementing, and managing an effective IPv4 addressing plan ensures that networks can operate effectively and efficiently.
For data communications to take place between devices in a network, the devices must be uniquely addressed.
Managing the addressing of these devices and understanding the IPv4 address structure and its representation are therefore, essential.

## Slide 19: IPv4 Addressing
Each device on a network must be uniquely defined by a network layer address.
At this layer, the packets (datagrams) of the communication are also identified with the source and destination addresses of the two end systems.
With IPv4, each packet uses a 32-bit source address and a 32-bit destination address in the Layer 3 header.

## Slide 20: IPv4 Addressing
These addresses are represented in the data network as binary patterns.
Inside the devices, digital logic is applied for the interpretation of these addresses.
For the human network, a string of 32 bits is difficult to interpret and even more difficult to remember.
For this reason, IPv4 addresses are represented using dotted decimal format.

## Slide 21: IPv4 Addressing
IPv4 addresses are easier to remember, write, and verbally communicate than strings of 32 bits.
Representing IPv4 addresses as dotted decimals begins by separating the 32 bits of the address into bytes.
Each byte of the binary pattern, called an octet, is separated with a dot.
The bytes are called an octet, because each of the decimal numbers represents 1 byte, or 8 bits.

## Slide 22: IPv4 Addressing
For example, the following address:
  10101100000100000000010000010100 is expressed in dotted format as 10101100.00010000.00000100.00010100
  And in decimal as 172.16.4.20.
  Keep in mind that devices use binary logic.
The dotted decimal format makes it easier for people to use and remember addresses.

## Slide 23: IPv4 Addressing
IPv4 addresses have two parts: the network portion and the host portion.
For each IPv4 address, some portion of the most significant bits, or high-order bits, represents the network address.
At Layer 3, a network is defined as a group of hosts that have identical bit patterns in the network address portion of their addresses.
That is, all the bits in the network portion of their addresses are identical.

## Slide 24: IPv4 Addressing
In the following example, the two addresses have identical network portions. Therefore, hosts assigned these two addresses would be on the same logical network:
172.16.4.20 172.16.4.32
network host network host
portion portion portion portion
Notes: Although all 32 bits define the IPv4 host address, a variable number of bits represent the host portion of the address. The number of bits used in this host portion determines the number of hosts within the network. In the previous example, the last octet, the lowest 8 bits, are the host portion. This means that the bits for the upper three octets represent the network portion.
You determine how many bits are required for the host portion based on the number of hosts that a network requires. If a particular network requires at least 200 hosts, you would need to use enough bits in the host portion to be able to represent at least 200 different bit patterns. To assign a unique address to 200 hosts, you would use the entire last octet. With 8 bits, a total of 256 different bit patterns can be achieved.

## Slide 25: IPv4 Addressing
Type of Addressing
  In IPv4 data networks, hosts communicate in three (3) different ways.
  These are unicast, broadcast and multicast.

## Slide 26: IPv4 Addressing
Type of Addressing
  Unicast
    The most common type of communication is unicast.
    This is the normal host-to-host communication in both a client/server and a peer-to-peer network.
    For unicast communication, the host addresses assigned to the two end devices are used as the source and destination IPv4 addresses.
    During the encapsulation process, the source host places its IPv4 address in the unicast packet header as the source host address and the IPv4 address of the destination host in the packet header as the destination address.
    The communication using a unicast packet can be forwarded through an internetwork using the same addresses.

## Slide 27: IPv4 Addressing
Type of Addressing
  Broadcast
    Broadcast communication is the process of sending a packet from one host to all hosts in the network.
    Unlike unicast communication, which uses the destination host address, broadcast and multicast communication use special addresses as the destination address.
    This special address, called the broadcast address, allows all the receiving hosts to accept the packet.
    When a host receives a packet with the broadcast address as the destination, it processes the packet as it would a packet to its unicast address. #

## Slide 28: IPv4 Addressing
Type of Addressing
  Broadcast
    Using these special addresses, broadcasts are generally restricted to the local network.
    Broadcast transmission is used for the location of special services/devices for which the address is not known or when a host needs to provide information to all the hosts on the network.
    Some examples for using broadcast transmission are as follows:
      Mapping upper-layer addresses to lower-layer addresses
      Requesting an address
      Exchanging routing information by routing protocols
Notes: When a host needs information, the host sends a request, called a query, to the broadcast address. All hosts in the network receive and process this query. One or more of the hosts with the requested information will respond, typically using unicast. Similarly, when a host needs to send information to the hosts on a network, it creates and sends a broadcast packet with the information.
Unlike unicast, where the packets can be routed throughout the internetwork, broadcast packets are usually restricted to the local network and not forwarded by a router. This restriction is dependent on the configuration of the router that borders the network and the type of broadcast.
There are two types of broadcasts: directed broadcast and limited broadcast. Each of these two types of broadcasts uses a different method of IPv4 addressing.

## Slide 29: IPv4 Addressing
Type of Addressing
  Multicast
    Multicast transmission is designed to conserve the bandwidth of the IPv4 network.
    It reduces traffic by allowing a host to send a single packet to a selected set of hosts.
    To reach multiple destination hosts using unicast communication, a source host would need to send an individual packet addressed to each host.
    With multicast, the source host can send a single packet that can reach thousands of destination hosts.

## Slide 30: IPv4 Addressing
Type of Addressing
  Multicast
    The following are some examples of multicast transmission:
      Video and audio broadcasts
      Routing information exchange by some routing protocols
      Distribution of software
      News feeds

## Slide 31: IPv4 Addressing
Type of Address
  In an IPv4 network, there are three types of addresses:
    Network address
    Broadcast address and
    Host address.

## Slide 32: IPv4 Addressing
Type of Address
  Network Address
    The network address is a standard way to refer to a network.
    This address cannot be assigned to a device and is, therefore, not used as an address for communication in the network.
    It is only used as a reference to the network.
    Within the IPv4 address range of a network, the lowest address is reserved for the network address.
    This address has a 0 for each host bit in the host portion of the address.

## Slide 33: IPv4 Addressing
Type of Address
  Broadcast Address
    The IPv4 broadcast address within a network is the directed broadcast address.
    Unlike the network address, this address is used in communication to all the hosts in a network.
    This special address for each network allows a single packet to communicate to all the hosts in that network.
    To send data to all hosts in a network, a host can send a single packet that is addressed to the broadcast address of the network.
    The broadcast address uses the highest address in the network range.
    This is the address in which the bits in the host portion are all 1s.

## Slide 34: IPv4 Addressing
Type of Address
  Host Address
    In an IP data network, every end device requires a unique unicast address to deliver a packet to that host.
    In IPv4 addresses, you can assign the values between the network address and the broadcast address to the devices in that network.
    These are called the host addresses.

## Slide 35: IPv4 Addressing
IPv4 Address Classes
  There are three popular IPv4 address classes defined by RFC 1700. These include:
    Class A
    Class B
    Class C

## Slide 36: IPv4 Addressing
IPv4 Address Classes
  Class A
    The class A address block was designed to support extremely large networks with more than 16 million host addresses.
    Class A IPv4 addresses used a fixed /8 prefix with the first octet to indicate the network address.
    The remaining three octets were used for host addresses.
    To reserve address space for the remaining address classes, all class A addresses required that the most significant bit of the high-order octet be a 0.

## Slide 37: IPv4 Addressing
IPv4 Address Classes
  Class A
    This meant that there were only 128 possible class A networks, 0.0.0.0 /8 to 127.0.0.0 /8, before taking out the reserved address blocks.
    Even though the class A addresses reserved one-half of the address space, because of their limit of 128 networks, they could only be allocated to approximately 120 companies or organizations.

## Slide 38: IPv4 Addressing
IPv4 Address Classes
  Class B
    Class B address space was designed to support the needs of moderate- to large-size networks with more than 65,000 hosts.
    A class B IP address used the two high-order octets to indicate the network address.
    The other two octets specified host addresses.
    As with class A, address space for the remaining address classes needed to be reserved.

## Slide 39: IPv4 Addressing
IPv4 Address Classes
  Class B
    For class B addresses, the most significant 2 bits of the high-order octet were 10.
    This restricted the address block for class B to 128.0.0.0 /16 to 191.255.0.0 /16.
    Class B had slightly more efficient allocation of addresses than class A because it equally divided 25 percent of the total IPv4 address space among approximately 16,000 networks.

## Slide 40: IPv4 Addressing
IPv4 Address Classes
  Class C
    The class C address space is the most commonly available of the historic address classes.
    This address space is intended to provide addresses for small networks with a maximum of 254 hosts.
    The Class C address blocks used a /24 prefix.
    This prefix meant that a class C network used only the last octet as host addresses, with the three high-order octets used to indicate the network address.

## Slide 41: IPv4 Addressing
IPv4 Address Classes
  Class C
    Class C address blocks set aside address space for class D (multicast) and class E (experimental) by using a fixed value of 110 for the three most significant bits of the high-order octet.
    This restricted the address block for class C to 192.0.0.0 /16 to 223.255.255.0 /16.
    Although it occupied only 12.5 percent of the total IPv4 address space, it could provide addresses to 2 million networks.

## Slide 42: IPv4 Addressing
Address Assignment
  Hosts are associated with an IPv4 network by a common network portion of the address.
  Within the network, there are different types of hosts, such as:
    End devices for users
    Servers and peripherals
    Hosts that are accessible from the Internet
    Intermediary devices

## Slide 43: IPv4 Addressing
Address Assignment
  Hosts are associated with an IPv4 network by a common network portion of the address.
  Within the network, there are different types of hosts, such as:
    End devices for users
    Servers and peripherals
    Hosts that are accessible from the Internet
    Intermediary devices

## Slide 44: IPv4 Addressing
Address Assignment
  Each of these different device types should be allocated to a logical block of addresses within the address range of the network.
  An important part of planning an IPv4 addressing scheme is deciding when private addresses are to be used and where they are to be applied.
  Any network resource, such as a server or a printer, should have a static IPv4 address.
  The client hosts access these resources using the IPv4 addresses of these devices.
  Therefore, predictable addresses for each of these servers and peripherals are necessary.
Notes: Servers and peripherals are a concentration point for network traffic. There are many packets sent to and from the IPv4 addresses of these devices. When monitoring network traffic with a tool like Wireshark, a network administrator should be able to rapidly identify these devices. Using a consistent numbering system for these devices makes the identification easier.
In most internetworks, only a few devices are accessible by hosts outside the corporation. For the most part, these devices are usually servers of some type. As with all devices in a network that provides network resources, the IPv4 addresses for these devices should be static.
In the case of servers accessible by the Internet, each of these must have a public space address associated with it. Additionally, variations in the address of one of these devices will make this device inaccessible from the Internet. In many cases, these devices are on a network that is numbered using private addresses. This means that the router or firewall at the perimeter of the network must be configured to translate the internal address of the server into a public address. Because of this additional configuration in the perimeter intermediary device, it is even more important that these devices have a predictable address.
Intermediary devices are also a concentration point for network traffic. Almost all traffic within or between networks passes through some form of intermediary device. Therefore, these network devices provide an opportune location for network management, monitoring, and security.
Most intermediary devices are assigned Layer 3 addresses, either for the device management or for device operation. Devices such as hubs, switches, and wireless access points do not require IPv4 addresses to operate as intermediary devices. However, to access these devices as hosts to configure, monitor, or troubleshoot network operation, they need to have addresses assigned.
Because you need to know how to communicate with intermediary devices, they should have predictable addresses. Therefore, their addresses are typically assigned manually. Additionally, the addresses of these devices should be in a different range within the network block than user device addresses.
Unlike the other intermediary devices mentioned, routers and firewall devices have an IPv4 address assigned to each interface. Each interface is in a different network and serves as the gateway for the hosts in that network. Typically, the router interface uses either the lowest or the highest address in the network. This assignment should be uniform across all networks in the corporation so that network personnel will always know the gateway of the network no matter which network they are working on.
Router and firewall interfaces are the concentration point for traffic entering and leaving the network. Because the hosts in each network use a router or firewall device interface as the gateway out of the network, many packets flow through these interfaces. Therefore, these devices can play a major role in network security by filtering packets based on source and/or destination IPv4 addresses. Grouping the different types of devices into logical addressing groups makes the assignment and operation of this packet filtering more efficient.
When addresses for devices are grouped by similar functions, you can create rules to address the group of devices instead of having to create individual rules for each device. A single rule can be created using a summary address rather than an individual rule for the address of each device. This allows the devices to have fewer security rules, which greatly streamlines the security function.

## Slide 45: IPv4 Addressing
Calculating IPv4 Addresses
  To work with IPv4 networks, you need to be able to develop and determine proper addressing.
  These skills include the ability to determine whether a particular host is on a network, determine the addresses in a particular network, and determine how to divide an addressing scheme for an internetwork.
  Inside data network devices, digital logic is applied for their interpretation of the addresses.
  When creating or forwarding an IPv4 packet, the destination network address must be extracted from the destination address. This is done by a logic called AND.
Notes: The IPv4 host address is logically ANDed with its subnet mask to determine the network address to which the host is associated. When this ANDing between the address and the subnet mask is performed, the result yields the network address.
ANDing is one of three basic binary operations used in digital logic. The other two are OR and NOT. While all three are used in data networks, AND is used in determining the network address. Therefore, the discussion in this section is limited to logical AND. Logical AND is the comparison of two bits that yields the following results:
1 AND 1 = 1
1 AND 0 = 0
0 AND 1 = 0
0 AND 0 = 0
The result from anything ANDed with a 1 yields a result that is the original bit. That is, 0 AND 1 is 0, and 1 AND 1 is 1. Consequently, anything ANDed with a 0 yields a 0. These properties of ANDing are used with the subnet mask to “mask” the host bits of an IPv4 address. Each bit of the address is ANDed with the corresponding bit of the subnet mask.
Because all the bits of the subnet mask that represent host bits are 0s, the host portion of the resulting network address becomes all 0s. Recall that an IPv4 address with all 0s in the host portion represents the network address. Likewise, all the bits of the subnet mask that indicate the network portion are 1s. When each of these 1s is ANDed with the corresponding bit of the address, the resulting bits are identical to the original address bits.

## Slide 46: IPv4 Addressing

## Slide 47: IPv4 Addressing
Calculating IPv4 Address
  The address calculation process requires you to examine these addresses in binary. Calculating the address assignments requires the following steps:
    Step One: Calculate the Network Address
      Determine the network address.
      The network address is the lowest address in the address block.
      To represent a network address, all the host bits are 0.
      With a 25-bit prefix, the last 7 bits are host bits and are 0s.
Notes: Each network range contains two important addresses that are excluded from the assignable network range to hosts or other devices. The first of these excluded addresses is the network address that represents a given network as opposed to a specific host within the network. The network address is identifiable by referring to the host field of the network address, in which the binary values within this range are all set to 0, for which it should also be noted that an all 0 binary value may not always represent a 0 value in the dotted decimal notation.
The second excluded address is the broadcast address that is used by the network layer to refer to any transmission that is expected to be sent to all destinations within a given network. The broadcast address is represented within the host field of the IP address where the binary values within this range are all set to 1. Host addresses make up the range that exists between the network and broadcast addresses.

## Slide 48: IPv4 Addressing
Calculating IPv4 Address
    Step Two: Calculate the lowest Host Address
      Next, you should calculate the lowest host address.
      This is always 1 greater than the network address.
      Therefore, using binary counting, you increment the 1s bit, making the last host bit a 1.

## Slide 49: IPv4 Addressing
Calculating IPv4 Address
  Step Three:
    Although it can seem a little out of sequence, it is often easier to calculate the broadcast address before calculating the highest host address.
    The broadcast address of a network is the highest address in the address block.
    It requires all the host bits to be set.
    Therefore, all seven host bits used in this example network are 1s.

## Slide 50: IPv4 Addressing
Calculating IPv4 Address
  Step 4: Calculate the Highest Host Address
    After determining the broadcast address, you can easily determine the highest host address. It is 1 less than the broadcast address
  Step 5: Determine the Host Address Range
    Finally, you need to determine the host range for the network.
    The host range of the network includes all the addresses from the lowest host address to the highest host address inclusive.

## Slide 51: Question!!!